## Slide 1
Zeroing the Z Axis

## Slide 2
For safety, turn router power switch to “OFF”

## Slide 3
Remove vacuum foot by pulling it down from router bracket. Set vacuum foot out of the way, to the side.

## Slide 4
Flip Z-Zero plate out from right side of handibot base.

## Slide 5
Move bit into place over Z-Zero plate.

## Slide 6
Remove bit clip from metal bracket on right side of tool.

## Slide 7
Attach clip to router collet.

## Slide 8
For safety, get your hands clear of the tool before starting the zeroing process!

## Slide 9
Tool will automatically touch off on Z-Zero plate and be offset based on the thickness of the handibot base.

## Slide 10
Be sure to put the clip back on the metal bracket on the right side of the tool.

## Slide 11
Flip Z Zero plate back into place on the tool base.

## Slide 12
Clip vacuum foot back onto router bracket.

## Slide 13
Turn router power switch back to “ON” to get ready to start cutting!